## Slide 1
MODULE 1 (M1)
TB BIOSAFETY

## Slide 2: MODULE CONTENTS
Transmission of TB bacilli
Risk assessment and precaution levels
Safety practices in the GeneXpert TB testing laboratory
Safe disposal of infectious waste

## Slide 3: LEARNING OBJECTIVES
At the end of this module, you will be able to:
    Understand the safety risks in laboratories using various methods
    Describe the risk associated with Xpert MTB/RIF (Ultra)* testing
    Explain what precautions should be taken to safely use Xpert MTB/RIF (Ultra) tests
    Create a spill kit for your laboratory
    Know how to safely clean up a spill outside or within the Biosafety Cabinet (BSC)
* Refers to Xpert MTB/RIF and Xpert MTB/RIF Ultra

## Slide 4: IMPORTANCE OF SAFETY IN THE LABORATORY
Following laboratory biosafety procedures prevents laboratory staff from becoming infected with TB and prevents microorganisms from being released into the environment

## Slide 5: TRANSMISSION OF TB BACILLI IN THE LABORATORY
The main risks in a TB laboratory are related to the aerosols generated during the procedures that could be inhaled by laboratory workers
The risk of aerosolisation is associated with the:
    Type of procedure
    Frequency of testing, and the laboratory’s workload
    Consistency of the material and its predisposition to aerosolize (for example, viscous liquids versus dry solids)
    Bacillary load of the materials

## Slide 6: PROCEDURES THAT CAN LEAD TO AEROSOLISATION
Placing specimens into a centrifuge and decanting supernatant
Handling clinical specimens
Mixing, pipetting or agitating fluids and/or cultures
Spills of clinical specimens and/or cultures
Breaking tubes/ flasks containing liquids

## Slide 7: RELATIVE RISKS FROM EXPOSURE TO INFECTIOUS TB
  Higher risk
Lower risk
Doctors and nursing staff in TB ward
Healthcare workers assisting with specimen collection
Couriers assisting with sample referral and transport
Technicians processing specimens for Xpert MTB/RIF and Xpert Ultra testing

## Slide 8: NEW APPROACHES TO BIOSAFETY ARE BASED ON RISK ASSESSMENTS
WHO has adopted an approach that assesses the risks associated with different technical procedures performed in different types of TB laboratories
  Risk-group classifications and containment levels (BSLs) are no longer used
  WHO’s biosafety manual* for TB laboratories describes minimum requirements for facilities, and the practices that can be adopted following a risk assessment
* http://apps.who.int/iris/bitstream/10665/77949/1/9789241504638_eng.pdf

## Slide 9: WHAT IS A RISK ASSESSMENT?
A risk assessment is a careful examination of what in your work could cause harm to people and must consider:
    Bacterial load of materials and the viability of TB bacilli
    The route of transmission of TB
    The epidemiology of the disease and the patient population
    Whether the handling and manipulations of clinical specimens and/or cultures are likely to generate infectious aerosols
    The number of manoeuvers that may generate aerosols
This slide may be considered optional for trainings of basic users

## Slide 10: WHAT IS A RISK ASSESSMENT?
A risk assessment is a careful examination of what in your work could cause harm to people and must consider:
    The workload of the laboratory and of individual staff members
    The location of the laboratory
    The level of experience and competence of lab staff
    The health of lab staff (especially HIV-positive staff)
This slide may be considered optional for trainings of basic users

## Slide 11: WHAT ARE THE STEPS IN CONDUCTING A RISK ASSESSMENT?
Identify potential hazards
Decide who might be harmed and how
Evaluate risks and decide on precautions:
    Determine the suitability of the physical space
    Evaluate the staff’s proficiency in following safe practices
    Evaluate the integrity of safety equipment
Record findings and implement any necessary changes
This slide may be considered optional for trainings of basic users

## Slide 12: RISK PRECAUTION LEVELS
According to the WHO TB Laboratory Biosafety Manual, risk precaution levels refer to the likelihood that specific laboratory procedures will result in a laboratory staff member becoming infected with TB
  Risk levels are assigned
    Low
    Moderate
    High

## Slide 13: RISK PRECAUTION LEVEL: LOW RISK
Risk level of TB laboratory | Laboratory activities | Assessment of risk
Low risk | Preparing specimens for smear microscopy or Xpert MTB/RIF test | Procedures have a low risk of generating infectious aerosols from specimens; the concentration of infectious particles is low
Moderate risk | Processing and concentrating specimens for Xpert assays testing or inoculation onto primary culture media; splitting specimens; direct DST (for example, LPA on processed sputum) | Procedures have a moderate risk of generating infectious aerosols; the concentration of infectious particles is low to moderate
High risk (TB-containment laboratory) | Culture manipulation for identification; DST or LPA on cultured isolates | Procedures have a high risk of generating infectious aerosols; the concentration of infectious particles is high

## Slide 14: BIOSAFETY REQUIREMENTS FOR XPERT MTB/RIF (ULTRA): OVERVIEW
The Xpert MTB/RIF (Ultra) are low-risk procedures when performed directly from sputum, and require the same level of precautions as those used for performing direct AFB sputum-smear microscopy
The addition of buffer inactivates M. tuberculosis bacilli in the sample, significantly reducing the biosafety risk to the laboratory technician
    Work in a well-ventilated area
    Wear gloves and a laboratory coat when handling samples
    Follow waste disposal guidelines

## Slide 15: BIOSAFETY REQUIREMENTS FOR XPERT MTB/RIF (ULTRA): OVERVIEW
    The Xpert MTB/RIF (Ultra) are moderate-risk procedures when performed from processed sediments
    Because of the risk of generating aerosols, splitting specimens and handling concentrated specimens must be performed within a certified Biological Safety Cabinet (BSC)
    In MDR-TB high burden areas, a risk assessment may determine that additional biosafety precautions are required; these precautions may include the use of N95 respirators or BSCs

## Slide 16: CLASSIFICATION OF LABORATORY ACTIVITIES: CLEAN OR DIRTY?
Clean activities are those which do not involve directly working with potentially infectious agents
Dirty activities are those which involve working directly with potentially infectious agents

## Slide 17: CLASSIFICATION OF LABORATORY ACTIVITIES: CLEAN OR DIRTY?
Are the following clean or dirty activities:
Sample reception
Processing samples for Xpert MTB/RIF (Ultra) testing, and inoculating cartridges
Loading cartridges into the GeneXpert instrument
Record keeping

## Slide 18: SAFETY PRACTICES
Use of bench spaces:
    The bench used to process specimens for direct sputum-smear microscopy or Xpert MTB/RIF (Ultra) tests (dirty) should be separate from areas where specimens are received and from areas where paperwork is completed and telephones are used (clean)
Ventilation:
    When appropriate microbiological techniques are used, processing of specimens for Xpert MTB/RIF (Ultra) may both be carried out on an open bench in an adequately ventilated area

## Slide 19: EXERCISE 1: LAYOUT OF THE TB LABORATORY
Purpose
To design the optimal layout of a TB laboratory performing smear and Xpert MTB/RIF (Ultra) testing
Total time
50 minutes- 15 minutes to complete the exercise; 5 minutes for each group to present their layout
Process
Divide into four groups
Review the TB laboratory layout diagram provided in the worksheets
Using scissors, cut out the pieces of equipment on Worksheet 2 (Equipment) and place them optimally on Worksheet 1 (TB Laboratory Layout)
Indicate the air flow and movement of staff
Share your findings with the group

## Slide 20: PERSONAL PROTECTIVE EQUIPMENT (PPE)
Gloves: essential (use gloves that are disposable and powder-free)
Lab coats: essential
Respirators:
Normally not required
  May be needed based on a risk assessment
  Must always be included in a spill kit
  Recommended respirators are N95 (NIOSH N95) and FFP2 (EN 149:2001)
Adapt according to NTP guidelines in your country

## Slide 21: PPE: GLOVES
Gloves are required for processing specimens for Xpert MTB/RIF (Ultra) testing:
    Use disposable gloves and maintain regular handwashing
    Wear a clean gloves when loading the GeneXpert
    To avoid contamination change to a clean gloves before using computers or cell phones
    DO NOT reuse gloves
    DO NOT wear gloves outside the laboratory
    Gloves should be discarded with infected laboratory waste
Adapt according to NTP guidelines in your country

## Slide 22: PPE: LABORATORY COATS
Laboratory coats are essential:
    Leave coats at the worksite
    Fasten the laboratory coat when worn
    Use appropriate size and type
    DO NOT wear outside of the laboratory
    Autoclave coats before laundering
    Launder at least weekly, and after any overt contamination (do not take the coat home)
Adapt according to NTP guidelines in your country

## Slide 23: PPE: RESPIRATORS
N95 and FFP2 respirators effectively filter out >94-95% of particles ≥0.3-0.4 µm in diameter
Respirators must be fitted to the face! (Use the FIT-TEST*)
Surgical masks do not protect the wearer against inhaling infectious aerosols
Respirators protect the wearer from inhaling droplet nuclei
(they protect against inhalation)
Surgical masks prevent microorganisms spreading from the wearer (they protect others from exhalation)
* https://www.osha.gov/video/respiratory_protection/fittesting_transcript.html

## Slide 24: DISINFECTANTS
A disinfectant is a chemical or mixture of chemicals used to kill microorganisms
Disinfectants are usually applied to surfaces or inanimate objects
Disinfectants may be used before autoclaving for pre-decontamination treatment
NOTE: Because of the specific cell-wall structure of TB bacilli, they are resistant to most standard disinfectants

## Slide 25: DISINFECTANTS
Disinfectants used in the TB laboratory must be effective against mycobacteria:
PHENOL (2-5%) in deionized water is highly irritating, caution must be used in preparation. It is preferable to use phenolic derivatives (e.g. triclosan, chloroxylenol, orthophenylphenol)
  Decontaminate equipment, surfaces and items or liquids before disposal (wear gloves)
  Prepare the solution daily and leave in contact with the surface for at least 15 minutes to ensure decontamination
Adapt according to NTP guidelines in your country

## Slide 26: DISINFECTANTS
The disinfectant used in the TB laboratory must be effective against mycobacteria
CHLORINE (sodium hypochlorite, or bleach with 0.72% active chlorine) is an irritant, and is corrosive to metals and plastics:
  It is a general purpose disinfectant; and can be used to soak items
  Allow at least 15 minutes to ensure decontamination
  Prepare daily and store in a well-ventilated area (toxic gas). Do not autoclave
Adapt according to NTP guidelines in your country

## Slide 27
The disinfectant used in the TB laboratory must be effective against mycobacteria
ALCOHOL (70%) leaves no residue but is volatile and flammable (keep far from open flames):
  Use as a disinfectant on skin (follow by washing with soap) and work surfaces (including metals)
PERACETIC ACID (working solution 2%) leaves no residue, but is stable for only 48 hours after preparation:
  Rapid action against all microorganisms
Adapt according to NTP guidelines in your country
DISINFECTANTS

## Slide 28: DISINFECTANTS PROS & CONS
Disinfectant | Pros | Cons
Phenol | Decontaminates equipment, surfaces and items or liquids before disposal | Highly irritating / carcinogenic
Bleach | Effectively kills mycobacteria / can be used to soak items | Corrosive to metals and plastics
Alcohol | Leaves no residue- use with other disinfectants to decontaminate surfaces (including metals) | Volatile and flammable
Peracetic acid | Kills mycobacteria & leaves no residue (see above) | Difficult to obtain / cost

## Slide 29: PREPARING DISINFECTANTS
  Often disinfectants come as a stock solution, or powder which must be prepared fresh before use
  For example, stock bleach is normally 4% concentration
  Cleaning the GeneXpert instrument requires 0.1% bleach (final concentration of chloride)
Notes: Handout only

## Slide 30: EXERCISE: PREPARING DISINFECTANTS
Purpose
Calculate the correct volume of bleach required to make a final concentration of bleach for cleaning the GeneXpert instrument
Total time
10 minutes – 5 minutes to work through the example, and 5 minutes to complete the exercise
Process
Working individually, review the example and complete the exercise using a calculator (or phone)
Share your findings with the group

## Slide 31: SPILL KIT
Instructions (SOPs) for cleaning up spills
A large biohazard bag (autoclavable)
Disinfectant (1% Bleach - freshly prepared)
Laboratory gowns (disposable) and goggles
Box of gloves (different sizes)
Respirators (N95 or FFP2)
Paper towels, cotton wool or absorbent cloths
Soap and chloramine tablets
Dustpan
Sharps container
“DO NOT ENTER” sign
All laboratories handling samples for TB diagnostic testing should have a spill kit
Check contents of the spill kit regularly and replace items after use or when they have expired

## Slide 32: SPILLS PROCEDURES
All personnel in the laboratory must be trained in the procedures for handling spills
The actions required depend on where the spill occurs:
    Outside a BSC
    Within a BSC

## Slide 33: SPILLS OUTSIDE OF A BSC
For spills outside of the BSC (including spilling sputum from a sample container):
Immediately vacate and secure the laboratory, and inform the laboratory manager
Leave the laboratory’s ventilation or exhaust systems on (i.e. BSC)
Do not re-enter the laboratory for at least 1 hour (post DO NOT ENTER signs)

## Slide 34: SPILLS OUTSIDE OF A BSC
Before re-entering the laboratory, put on clean gloves, a clean gown and a respirator
Cover the spill with cloths or absorbent paper, and soak the paper with a suitable disinfectant; apply the disinfectant concentrically, from the outer margin towards the centre of the spill
Allow sufficient time for the disinfectant to act (at least 30-60 minutes) before disposing of any material

## Slide 35: SPILLS OUTSIDE OF A BSC
Collect all containers, clean-up material and place them in the disposal bag provided in the spill kit; tie the disposal bag and place it in a container to be autoclaved (use an appropriate container for sharp objects)
Change gloves if they have been contaminated; dispose of these along with other infectious waste
Clean and disinfect the area of the spill with bleach
Staff exposed to the spill should be referred for medical advice, and details recorded in the incident logbook

## Slide 36: SPILLS INSIDE THE BSC
Clean up should begin immediately and the cabinet should continue to operate
Cover the spill area with cloths or absorbent paper, and apply disinfectant concentrically (from the outer margin towards the centre of the spill)
Equipment or material that has been splashed must be cleaned (including the interior surfaces and walls of the BSC, or safety buckets)
Disinfect metal objects with Phenol, alcohol 70%, or Peracetic Acid (not bleach- it’s corrosive!)
Allow sufficient time for the disinfectant to act (30-60 minutes) before disposing of any material

## Slide 37: SPILLS INSIDE THE BSC
Within the BSC, place all containers and clean-up material into the disposal bag provided in the spill kit; tie the bag, and place it in a container to be autoclaved
Change gloves; dispose of these along with other infectious waste
Staff exposed to the spill should be referred for medical advice, and details recorded in the incident logbook

## Slide 38: WASTE DISPOSAL
At the end of each day, seal contaminated material (such as used sputum containers, transfer pipettes and used cartridges) in a biohazard bag
    Commonly, waste is autoclaved, incinerated or buried
    Consult your institution’s environmental waste policy regarding proper disposal of used cartridges and unused reagents
  Warning: incinerating plastics can release toxins that are harmful to breathe
Adapt according to NTP guidelines in your country
Notes: LINK NEEDS TO BE UPDATED

## Slide 39: SAFETY TRAINING
Safety training of staff is an important component of providing a safe working environment:
    Staff should be trained to recognize TB symptoms at induction, and periodically thereafter
    Health monitoring should be provided, and include a baseline medical check-up, a Health Questionnaire which must be completed quarterly, and chest X-ray / skin testing annually
    Minimum training for visitors, students, clerical & support staff (including couriers and drivers) should be provided; and include the risks associated with working with MTB in the laboratory; the laboratory layout, donning PPE, recognizing the signs & symptoms of TB, what to do in the case of an emergency and dealing with spills in the TB laboratory

## Slide 40: SAFETY AUDITS
It is recommended that the TB Laboratory review safety procedures systemically and frequently throughout the year
Audit of all procedures and their implementation
Document the biosafety audit process and identifying mitigation measures to ensure that safety in the laboratory is constantly improved
A checklist for conducting safety audits can be found in WHO’s biosafety manual for TB laboratories*
* http://www.who.int/csr/resources/publications/biosafety/who_cds_csr_lyo_20034/en/
Notes: LINK NEEDS TO BE UPDATED

## Slide 41: DISCUSSION QUESTIONS
What are the sources of infectious aerosols in a TB laboratory?
What is the level of risk for performing Xpert MTB/RIF or Xpert MTB/RIF Ultra testing?
What precautions must be taken when handling specimens for performing Xpert MTB/RIF or Xpert MTB/RIF Ultra testing?
What are the contents of a spill kit?
What are the steps for safely disposing of infectious waste?

## Slide 42: KEY MESSAGES
The Xpert MTB/RIF (Ultra) test is a low-risk procedure when performed directly from sputum. Testing requires the same precautions as used for microscopy
The main risks in a TB laboratory are related to the generation of aerosols
A BSC is required when splitting samples or handling concentrated specimens
Disinfectants should be selected based on their tuberculocidal activity and the material to be disinfected
Ensure that the laboratory is prepared for emergencies and has standard operating procedures for handling accidents such as spills

## Slide 43
THANK YOU
© John Rae