## Slide 1: Line-Probe Assay CM interpretation
<number>

## Slide 2: Overview of the principle of reverse hybridization
<number>

## Slide 3: Two internal controls on each strip
Both bands must be present for a valid test
Band 1 - Conjugate Control (CC)
  Indicates the binding of substrate to the conjugate during hybridization
  Hybridization worked
Band 2 - Universal Control (UC)
  Indicates mycobacteria and other gram-positive bacteria with a high G + C content
  Amplification control – PCR worked
<number>

## Slide 4: Interpretation of CM strip
Genus Control band – GC
  Mycobacteria species-specific
  May be weak or absent
    Test is valid
    Identify species if species-specific bands are present and GC is absent
Other bands
  Species-specific bands
<number>

## Slide 5: Identification with species specific bands
Record the number corresponding to the species-specific bands on worksheet
Find bands on the interpretation chart
Record identification
Some species are closely related and CM cannot distinguish between them
  Record identification as indicated on the chart
<number>

## Slide 6: Interpretation of results (CM)
Interpretation of banding
Bands 1, 2, 3 = Mycobacterium species
Bands 1, 2, 3, 4 = M. avium ssp.
Bands 1, 2, 3, 10, 16 = MTB complex
Bands 1, 2, 3, 14 = M. peregrinum
Bands 1, 2, 3, 17 = M. xenopi
<number>

## Slide 7: CM: ID of 14 species + MTB AS: ID of 16 species
<number>

## Slide 8: Acknowledgement
<number>