## Slide 1: Identification of the Mycobacterium tuberculosis complex by the Molecular Line-Probe Assay

## Slide 2: Different Line Probe Assays that will identify the MTB complex
CM/AS common mycobacteria and additional species
  Species identification of the MTB complex and 30 other Mycobacterium species (2 strips)
MTBC
  Differentiation of the members of the MTB complex
MTBDRplus (multidrug resistant)
  Identification of MTB complex and mutations associated with INH and RIF resistance
MTBDRsl (Extensively drug resistant)
  Mutations associated with fluoroquinolone, aminoglycoside and EMB resistance
<number>

## Slide 3: The Line Probe Assay Kits have different primers and probes
Kit components are specific for each of the line-probe assays
  Kit-specific primers
  Kit-specific probes on the strips
Primers from one kit or type of assay cannot be used with strips from another kit
  Invalid results
<number>

## Slide 4: Line Probe Assay steps
DNA extraction
  Sample
Amplification
  PCR
Hybridization
  Detection
<number>

## Slide 5: DNA preparation
DNA sample
  Processed sputum sediment
  Culture
Heat-kill bacteria
  Sample heat-killed in culture laboratory before moving to molecular laboratory for DNA extraction
DNA extraction
  sonication
<number>

## Slide 6: PCR
PCR reaction using cells from AFB isolate
  Primers are labelled with biotin
  Biotin-labelled primers are incorporated into the amplified target DNA sequences during PCR
  More than one primer set is used in the same reaction
    Several labelled target sequences are amplified at the same time
<number>

## Slide 7: Hybridization-detection
Reverse hybridization
  Unlabelled probes specific for MTB complex or other mycobacterial species are bound to strips
    Several target sequence probes can be placed on a strip
  Biotin-labelled target DNA binds to complementary probe on strip
Probe-target complex is detected
  Streptavidin-conjugated reagent detects biotin-labelled probe-target complex
<number>

## Slide 8
PCR is a technique that takes a small amount of a specific DNA sequence and amplifies it for further testing
It has been called a “molecular photocopier”
PCR was invented by Kary Mullis in 1983
(Nobel Prize for Chemistry in 1993)
Polymerase Chain Reaction (PCR)
<number>

## Slide 9: Major components of a PCR reaction
Primers – short pieces of DNA needed to start DNA synthesis by binding to specific regions of target DNA
  DNA polymerase requires primers to begin extension
Deoxynucleotides (dNTPs) – building blocks for DNA synthesis
  dATP, dTTP, dCTP, dGTP
DNA polymerase – enzyme for DNA synthesis
Buffer - provides optimal conditions for the activity of DNA polymerase
PCR performed in a Thermal cycler
<number>

## Slide 10
human
DNA polymerase
Taq
DNA Polymerase
Some like it hot!
Taq DNA polymerase has been isolated from the bacterium Thermus aquaticus from hot springs at Yellowstone Park – this enzyme was needed to optimize PCR
72oC
37oC
Taq DNA polymerase loves heat!
Most DNA polymerases don’t work at high temperatures
<number>

## Slide 11
Primers are sequence-specific oligonucleotides that hybridize to the target DNA and serve as a starting point for the DNA polymerase to add nucleotides
Forward and reverse primer set flank the target sequence and allow both DNA strands to be copied simultaneously in both directions.
Primers
<number>

## Slide 12
PCR reaction components
DNA polymerase
Forward DNA primer
Target DNA
dNTPs – G A T C
Reverse DNA primer
<number>

## Slide 13: Three steps of PCR
Denaturation
  Increase temperature, bonds break between the base pairs, strands separate
Annealing
  Decrease temperature, primers bind to complementary sequence on DNA strands
Extension
  Increase temperature, DNA polymerase adds dNTPS to strands
<number>
1 cycle = 3 steps

## Slide 14
3´
5´
5´
3´
5´
5´
3´
3´
3´
3´
5´
5´
5´
3´
5´
3´
Target gene
Denaturation at 94-95 oC
Primer annealing at 58-65 oC
Extension at 72 oC
DNA polymerase
DNA polymerase
Plus dNTPs G A T C
First cycle in the Thermal cycler instrument
<number>

## Slide 15: 35 Cycles: Billions of copies of target are made
<number>

## Slide 16
Overview of reverse hybridization
4. Binding of enzyme-conjugated protein
5. Enzymatic conversion of dye and visualization of positive bands
1. Separation of amplicons into single-stranded DNA
3. Removal of amplicons that don’t match exactly
2. Binding of labelled amplicons to probes on strips
Substrate reaction
Denaturation
Hybridization
Stringent wash
Conjugate reaction
<number>

## Slide 17: Denaturation of dsDNA amplicons
<number>

## Slide 18: Hybridization of ssDNA amplicons
<number>

## Slide 19: Stringent washing of strips
A.
B.
<number>

## Slide 20: Streptavidin binding to bound Amplicon
<number>

## Slide 21: Substrate reaction / colour development
z
substrate
colourless
substrate
brown
DNA•STRIP®
<number>

## Slide 22: Interpretation of results (CM)
Interpretation of banding
Bands 1, 2, 3 = Mycobacterium species
Bands 1, 2, 3, 4 = M. avium ssp.
Bands 1, 2, 3,10,16 = MTB complex
Bands 1, 2, 3,14 = M. peregrinum
Bands 1, 2, 3, 17 = M. xenopi
<number>

## Slide 23: CM: ID of 14 species + MTB AS: ID of 16 species
<number>

## Slide 24: Banding patterns on strips
<number>

## Slide 25: Quality control of LPA
The following controls must be included in each PCR run to ensure quality results
  Positive processing control
    Well characterized isolate of M. tuberculosis
    1:100 dilution of 0.5 McFarland growth solution
  Negative processing control
  Negative amplification monitoring control
    Contamination control
<number>

## Slide 26: Quality assurance
Monitor the number of species isolated
  Number of MTBC
  Number of NTM
    By species
Monitor contamination rate
  Negative processing control
  Negative amplification control
Wipe test for contamination
<number>

## Slide 27: Acknowledgement
<number>