## Slide 1: Quality assurance for LPA: What is necessary, what is possible?
<number>

## Slide 2
<number>
Quality Assurance
Quality Control
External Quality
Assessment

## Slide 3
<number>
Infrastructure QC
Adding DNA
Specimen preparation
Hybridization
Reagent preparation
Sentinel testing:
1ml molecular-grade water
in 1.5 ml at different areas for 24h

## Slide 4: Equipment QC: books of life
<number>
Each instrument requires specific knowledge to properly calibrate, operate and maintain
Establish preventive and corrective maintenance
Procedures must be followed exactly
  To ensure safety in the laboratory
  To ensure proper functioning of
  the instrument
Daily usage logs, corrective action logs, repair and maintenance records must be recorded in log books kept for each instrument

## Slide 5: Reagent QC
<number>
Lot-to-lot testing
Integrity testing upon receipt (e.g.Taq polymerase)
Storage in customs
Proper supply chain (cold chain) including in-country distribution

## Slide 6: Procedure QC (1)
<number>
SOPs
Controls
  Inactivated MTB/BCG control for entire procedure (specimen preparation)
  Negative control for MM preparation
  Negative control for specimen preparation
Contamination control
  Tools
  Reagents
  Infrastructure
  Procedure

## Slide 7: Procedure QC (2) The question of positive control
<number>
Interpretation of results
  adequate runs
  inadequate runs

## Slide 8: Procedure QC (2) Negative control for specimen processing
<number>

## Slide 9: Procedure QC (3) Quality indicators
<number>
Implementation and quarterly monitoring of quality indicators
  Monitor the number (%) of unsuccessful amplifications for AC/ TUB rpoB/katG/inhA
  Monitor the number (%) of different mutation “types” (common and uncommon)
  Monitor the number (%) of tests with mixed pattern (rpoB/katG/ inhA)
  Monitor turn-around time
  Culture and drug susceptibility testing of all specimens with resistant results
  Culture 10% of specimens with susceptible result
  Confirm discrepant results (molecular vs conventional) by other molecular and conventional method if possible

## Slide 10: Personnel QC
<number>
Record specimens that were processed (NALC/ NaOH) and molecular tested in the same batch
Record specimens tested in one batch and technician who performed the run
Train and re-train

## Slide 11: External quality assurance (EQA)
<number>
Panel testing
  Entire procedure including specimen preparation and NaOH/NALC processing
  Susceptible strain
  Resistant INH mono, RMP mono
  MDR (common and uncommon mutations)
  NTM strains
  Costs and QA (preparation, shipment, data evaluation and feed-back)

## Slide 12: EQA
<number>
Proficiency testing (training and routine)
  Using duplicate specimens (A and B) of same patients

## Slide 13
<number>
Proficiency testing for LPA:
India
 | Proficiency testing round | Negative control | Invalid results (number invalid/total number, %) | Internal concordance (same patient, same laboratory)* | External concordance (same specimen, different laboratory)*
Benchmark |  | Clean | < 10% | > 95% | > 95%
Lab A | 1st | Failed | 14/48 (29%) | - | -
 | 2nd | Clean | 15/22 (70%) | - | -
 | 3rd | Clean | 5/118 (4%) | 54/54 (100%) | 19/19 (100%)
Lab B | 1st | Clean | 15/100 (15%) | 36/37 (97%) | 17/17 (100%)
 | 2nd | Clean | 2/30 (6%) | 14/14 (100%) | -
Lab C | 1st | Clean | 7/102 (7%) | 44/44 (100%) | 18/20 (90%)
Lab D | 1st | Failed | 24/96 (25%) | 48/48 (100%) | 19/20(95%)

## Slide 14: EQA
<number>
EQA of interpretation
  picture bank (unusual, good and bad results)
  paper- or online-based testing (e-learning)
  blinded re-checking of scanned results

## Slide 15: Face the problem and find the best solution Bronchoscopy of a Siberian tiger with TB
<number>

## Slide 16: Acknowledgement
<number>