## Slide 1: Module RECHECKING PROCEDURES

## Slide 2: Content Overview
Keeping and collecting the slides
Restaining the slides
Reading the slides
Evaluating the smear quality

## Slide 3: KEEPING THE SLIDE BOXES AND SELECTING THE SAMPLE

## Slide 4: Keeping the Slide Boxes (1)
STEPS:
Label slides with lab. number and result column number or code
After slide reading
    Let oil soak into absorbent paper by putting slides with smear downwards on strip of toilet paper or news paper
    Do not remove oil with xylene or other solvent
    Do not rub
Keep slides of all patients until sample is taken

## Slide 5: Keeping the Slide Boxes (2)
STEPS
Arrange slides in boxes according to serial number
Leave empty slots for specimens not yet examined (2nd, 3rd diagnostic smear)
Start filling new boxes each quarter
Ensure sufficient boxes for slide storage for 2 quarters
Notes: Correct slide keeping is not always easy. Discuss the practicalities and implications for large laboratories with the participants. Try to come up with solutions accepted by the NTP and lab services.

## Slide 6: Sample Selection (1)
Sample collection by TB supervisor, never by laboratory staff
Feedback on previous EQA performance to motivate lab staff to keep slides and improve performance if applicable
If sampling during visit not possible:
  forward all slides and copy Lab. Register to rechecking coordinator for sample taking, filling forms and forwarding to first controller
Notes: Customisation: specify here the designation of the TB (non-lab specialist) supervisor responsible for sample collection, the first controllers, and the coordinators.

## Slide 7: Sample Selection (2)
Collect during each visit fraction of sample covering period since last visit
Mark period in Lab. Register, draw line under last entry of the period
Count total number of smears examined during the period, or use numbers recorded by lab.staff
Calculate sampling step by dividing total number of smears by required sample size
  e.g. 675 smears examined, 24 samples to take, gives sampling step of 675/24= 28
Notes: Customise this slide: specify the annual sample size, the frequency and number of slides to be collected per visit.
Explain that the sample should be selected in the register and not directly from the boxes, as a check on the completeness of the slide keeping. If many slides selected from the register are not found in the boxes, this means that keeping slides is unsatisfactory and the samples cannot be considered as representative. Stress that the sampling step must be calculated and applied disregarding the results of the smears (positive, negative, scanty).

## Slide 8: Sample Selection (3)
Fill two blinded rechecking forms of sputum smear examinations for AFB
  one form with and one without smear results
Use random number, e.g. last digit of bank note to select first slide.
  If 5, the first slide is the 5th in Lab. Register.
  The second slide is the 33rd slide, and so on, until 24 slides have been selected

## Slide 9: Sample Selection (4)
Note identification number of the slides on the rechecking form
Request staff of the centre to retrieve the selected slides from the slide boxes
Check slides against the list
Mark missing slides on the form; replace missed slide with next slide in Lab. Register
Ensure that each slide has identification number

## Slide 10: Sample Selection (5)
If no slides with positive/scanty results in the sample, add first two positive/scanty slides in Lab. Register from start of the period
Ensure that all not selected slides are discarded
Arrange slides in transport box in order of the form, and give box, together with copy of the form without the results to first controller
Give form with results to rechecking coordinator
Notes: Customisation: specify here the designation of the coordinators.
Stress that positive and negative slides should be arranged according to numbering, also in the boxes that are sent to the controllers, to avoid possible unblinding. This applies particularly to positives added to the list afterwards.

## Slide 11: RESTAINING THE SLIDES
Notes: Customisation: the whole part on restaining up to slide 17 may have to be omitted or modified depending on your national policy regarding restaining. Please refer to the customisation chapter in the trainer's manual. Restaining of auramine stained smears with auramine before any control reading will always be needed (slide 18 and 19)

## Slide 12: Ziehl-Neelsen (ZN) Stained Slides (1)
Fuchsin stain fades with high temperature and high humidity
Speed of fading is unpredictable
More extreme on low positives and poorly stained smears, not only in extreme climates

## Slide 13: Ziehl-Neelsen (ZN) Stained Slides (2)
Consequences of fading of fuchsin stain
  FP reported by first controller and/or second controller
    False accusations
  Missed low positives at microscopy centre not identified as FN by first controller and/or second controller
    Positive patients not identified
Notes: Customisation: specify here the designation of the first and second controllers, if possible.

## Slide 14
Notes: Explain that fuchsin staining fades more or less rapidly in function of temperature and relative humidity (RH). This chart shows the results of an experiment where smears were kept at various temperatures and RH with repeated readings till all AFB had become invisible.

## Slide 15: Ziehl-Neelsen (ZN) Stained Slides (3)
Options when fading may be a problem
1. Restaining of all discordant slides at the second control level
But restaining of all sample slides is needed if:
  first controllers miss many scanty and 1+
  and/or quantifications are systematically lower for first controllers
Notes: Restaining is often considered as too tedious, but it may be indispensable to arrive at the correct conclusions. At least all discordants should be restained before second control reading is done, and its effect needs to be analysed. If this restaining makes many positives reappear (true positives seen in the periphery and at second control after restaining, but missed by the first controller without restaining), false negatives will also have been impossible to detect. The same conclusions may have to be drawn if quantifications become systematically higher after restaining.

## Slide 16: Ziehl-Neelsen (ZN) Stained Slides (4)
2. Restaining of all slides at the first control level
Advised if
  Quality of staining solution not well controlled; no control on chemicals
  Decentralized preparation of solutions
Advantages
  Detection of gross deficiencies of staining or staining solutions
  Takes care of fading
Disadvantages
  Increased work load for controllers
  May remove rare AFB
  May bring contamination with saprophytic AFB into evidence

## Slide 17
Notes: This is an example of how restaining can totally change the conclusions from rechecking, from a country without extreme climatic conditions. Slides were examined twice by the controllers, before and after restaining. Before restaining, many false positive but few false negatives were detected, conclusion would be that technicians don’t know AFB and need retraining. But the reverse was true after restaining, the problem was not need of training but poor staining and poor microscopes.

## Slide 18: Auramine Stained Slides
Restaining of all slides at the first control level
Restaining of discordant slides at the 2nd control level if slides not protected against fading since restaining at the 1st control level
Justified based on experience, anecdotal evidence and theoretical considerations
Notes: Stress that repeated restaining should be avoided, since it may remove AFB from thin smears. So once restained smears should be kept protected from light and high temperature / humidity, for ZN as well as FM rechecking.

## Slide 19: Restaining Technique
Remove the oil from the slides
No need to decolorize
Restain with same staining solution type and same staining cycle as in routine
Notes: Stress also that it is imperative to use the best possible quality of staining solutions (quality of reagents as well as preparation). If the NTP cannot control quality during procurement, discuss how quality could nevertheless be checked.

## Slide 20: READING THE SLIDES AND EVALUATING THE SMEAR QUALITY

## Slide 21: Reading the Slides (1)
First level rechecking is completely blinded
  First controller has no access to the results
  Only slides and copy of rechecking form with identification numbers are provided

## Slide 22: Reading the Slides (2)
Clean all oil-immersion examined slides with xylene
If slides are routinely restained at the first control level:
    Inspect smears with naked eye
    Write appreciation on size, thickness, evenness and background color
    Note that restaining was done
If slides are not routinely restained at the first control level:
    Write appreciation on size, thickness, evenness,
    AFB color and artefacts after microscopic reading

## Slide 23: Reading the Slides (3)
Restain all auramine stained slides
Restain all ZN stained slides, if NTP policy
Check smears using original microscope: bright field for ZN, fluorescence for FM and standard magnification
Check same number of fields as in routine- usually 100 fields or one length
Notes: Customisation: adapt to the national policy on restaining

## Slide 24: Reading the Slides (4)
Note results on copy rechecking form in column” first controls”
Add overall appreciation on smearing and staining at bottom of form
Do not recheck slides with unclear identification or severely damaged smears; report as excluded/ID or excluded/damaged

## Slide 25: Reading the Slides (4)
Let oil soak in paper (toilet paper, news paper), do not rub
Re-arrange slides in original box
Keep box in fridge if fading is expected
Send rechecking form to rechecking coordinator

## Slide 26: Evaluating Smear Quality
Smear quality concerns
  quality of specimen: real sputum or saliva
  quality of smear: size, thickness, evenness
  quality of staining: color of AFB and background

## Slide 27: Smear Quality (1)
Equal spreading of the material over an area of 2 cm by 3 cm or 2 cm by 1 cm
Microscopic appearances
  good sputum: mucus threads with white blood cells
  bad sputum: thin smear with epithelial cells
Follow-up smear may be saliva
Remarks on poor quality smear only if several thin smears without white blood cells
Notes: Customisation: keep only the standard smear size in your programme

## Slide 28: Macroscopic Appearance of a Good Smear
Notes: Stress the importance of equal spreading of the material over an area (describe size as specified by your programme).

## Slide 29: Macroscopic Appearance of a Poor Slide (1)

## Slide 30: Macroscopic Appearance of a Poor Slide (2)

## Slide 31: Macroscopic Appearance of a Poor Slide (3)

## Slide 32: Macroscopic Appearance of a Poor Slide (4)

## Slide 33: Staining Quality
A well stained ZN smear shows strong red AFB against a weak blue background
A well stained auramine smear (FM) shows yellowish fluorescent rods against a dark background
Background should not show much remaining red (ZN) or fluorescence and no red or fluorescent artifacts

## Slide 34: Stained Smears

## Slide 35: Smear Quality Report
Note qualitative aspects of smearing and staining
There will always be some less good smears, but no serious problem if no errors are found

## Slide 36: Key Messages
Slides from all patients, irrespective of their results, should be kept in the laboratories until sampling is done
Fading of fuchsin staining can falsify the results of rechecking. Restaining prior to controls may be needed for ZN, and is always needed for auramine stained smears.
First level rechecking must be completely blinded