## Slide 1: Module BACKGROUND AND PRINCIPLES OF RECHECKING

## Slide 2: Content Overview
Background of rechecking
Principles of rechecking

## Slide 3: Background Of Rechecking (1)
Purpose of rechecking
  Screening for possible problems of AFB microscopy in sample of smears examined in routine work
Aim of rechecking
  Improving quality of AFB microscopy
  Not correction of diagnoses
  Not substitute for internal quality control
  Not substitute for regular supervision
Notes: Stress that rechecking of samples of the routine work aims at identifying labs that may have problems, with the aim of solving them, and in that way improving the quality. It is too slow to correct diagnoses. It is complementary to internal quality control and can be used as a tool for targeted supervision, but it can not replace these two other components of the quality assurance system. Make it very clear that the aim is to support, but not to punish for errors that are sometimes unavoidable or that may be due to factors out of control of the technicians.

## Slide 4: High Quality AFB Microscopy
Essential for proper patient management
  Missed diagnosis of AFB-pos. patient (false negative=FN) or delayed diagnosis: death or advanced, disabling, disease
  Incorrect diagnosis as AFB-pos. (false positive=FP): drug side effects, social and economic consequences
Notes: This slide explains the consequences of false positive or false negative results for the patient and the community.

## Slide 5: Rechecking Merits
It shows what happens in practice
Can be highly motivating if done correctly

## Slide 6: Rechecking Disadvantages
Workload, especially for intermediate and central levels
Impossible in highly decentralized microscopy service or very low TB prevalence
Notes: Explain that the workload is proportional to the number of centres to be controlled and inversely proportional to the prevalence of positive smears in the laboratories. Thus the more labs a controller has to recheck and the lower the TB prevalence, the higher the workload. This is a strong argument against excessive decentralization.

## Slide 7: Principles Of Rechecking (1)
Random, representative, sample of slides from each laboratory is rechecked
Rechecking is blind: rechecker (=first controller) does not know results of the laboratory
Discordant slides (pos. at laboratory and neg. by rechecker, or the reverse) are rechecked by second controller (gold standard)
Errors assigned to laboratory or first controller
Notes: Explain the outline of the process. Stress that not all slides are checked by a second controller, but only those with a discordant result between peripheral lab and first controller. The results given by the second controller is considered as the correct one, so this controller has to be very reliable.
Stress that this is necessary since also first controllers make some mistakes, the result of the second controller will thus be used to define what is the error and who made it (peripheral lab or first controller). Till then, we can only speak of discordants and no feedback on errors can be given.
Giving all slides to a second controller again will overload this controller so that the results will not be more reliable and only add to confusion.

## Slide 8: Principles Of Rechecking (2)
Analysis to identify centers that may perform below standard
This needs to be confirmed by further checks and on-site visits
Identification of possible sources of errors and need for remedial action
Notes: This slide shows the next part of the cycle of rechecking.
Stress that not all labs that have errors may perform below standard, so an in-depth analysis has to be made according to pre-set criteria to identify those which are more likely to do so (because there may be a problem with the microscope, stains or staining, reading etc..) Then a selection has to be made of the labs that need a problem-identification and –solving visit by an expert. These will be the labs with the poorest performance. The others with only slightly too many errors may not have a real problem, or only a minor one such as slightly superficial reading. These labs will be followed-up by further rechecking, and visits will be made only if the excessive number of errors persists. The aim of the visits must be to probe into the causes of the errors, and it should result in solving them so as to prevent further errors.

## Slide 9: Prerequisites For Rechecking
A well functional TB programme
  Regular supervision
  Highly functional TB laboratory network, particularly at intermediate level
  Possibility for corrective actions
  (Additional) resources: personnel, materials, funds

## Slide 10: Inputs For Rechecking (1)
Personnel
  Supervisors for sample collection and feedback
  Rechecking coordinators at intermediate levels
  National level coordinator
  First level controllers
    Sufficient time
    Motivated
    Seniority not required
  Second level controllers
    Experienced, dedicated
    Sufficient time
    High level qualifications/position not required
Notes: This slide shows the staff input required for succesful rechecking, which are high. Stress that without excellent collaboration of all these people rechecking may be a waste of time. The supervisors collecting samples should be NTP general supervisors regularly visiting all TB centres, lab staff can better be used for other tasks. Also the intermadiate coordinator can better be a general TB programme officer. At national level, usually the coordination will be assured by the National Reference Laboratory. Stress the requirements to guide selection of the controllers. Note that this task requires sufficient time, so that high-level lab staff are usually not suitable.

## Slide 11: Inputs For Rechecking (2)
Materials and funds
  Microscopy centre
    Slide boxes, pencils/diamond markers
  Supervisors collecting the slides
    Slide boxes, sampling forms, transport
  Controllers
    TIME, staining facilities/equipment, transport
  TB coordinators
    Forms, tools for analysis (computer), transport
Notes: It is important for good collaboration and slide identification that the labs have proper materials such as slide boxes and diamond pencils (unless frosted slides are used). Stress the requirements to guide selection of the controllers. Note that this task requires sufficient time, so that high-level lab staff are usually not suitable. A computer at intermediate level and staff knowing EXCEL is the idela for data storage, transmission and analysis, particularly in a large country. However, at intermediate level this can be done also manually, with computerization only at national level.

## Slide 12: Sample Size Concepts (1)
Random, representative selection of any slide, irrespective of result and type (diagnostic, follow-up)
Fixed number of slides per laboratory per year
Sample size based on statistical system called Lot Quality Assurance Sampling (LQAS)
Notes: Explain that ideally there is only one uniform sample size, but that sometimes the National Reference Laboratory/NTP management may decide to use more than one sample size of slides for rechecking. This may be decided in case of wide variation in the number of smears examined by the labs and/or wide variation in the percentage of positive slides.

## Slide 13: Sample Size Concepts (2)
LQAS allows selection of the smallest possible sample for assurance of the quality of laboratories
Sample size is usually between 40 and 90 slides annually per lab
Notes: Explain that the LQAS system is particularly suitable for this purpose since it allows to conclude if a pre-set level of quality is reached after checking a small sample from the routine work. But it does not result in accurate error rates per lab, so that comparisons of individual labs are only approximate. However, for all the labs of a larger area or country these rates will be accurate also and can be compared.
The sample sizes are determined at national level, not by the different administrative areas or supervisors, who do not need to know the details of the system.
Customisation: specify here the annual sample size or selection of sizes for your country, and how it should be divided over the year, with for instance a quarterly sample size.

## Slide 14: Sample Size Concepts (3)
Number of false negative (FN) allowed in the sample is set at 0 (= no FN allowed)
  If no FN: quality of the centre is acceptable
  If >0 FN: not sure that quality of the centre is acceptable, further investigation needed
Clear-cut false positive (FP, i.e. 1+, 2+, 3+) are also not allowed

## Slide 15: Comparison of Sample Sizes: New and Old Method
Compared with old rechecking method- all positives and 10% of negatives- the sample size of LQAS method is much smaller
Notes: This slide shows a comparison of sample sizes using the in the past frequently applied sampling of all positives +10% of negatives, versus LQAS samples sizes taken from the LQAS samplesize tables. Stress that LQAS samples are smaller except if positivity rates are very low or labs have very low workload. All three labs in this example have either high positivity rates (first one)or high workload (other two). Stress also that the samplesize required for labs with high workload can be very small with LQAS, and that more are not required to detect poor performance due to problems. However, with low positivity rates more slides need to be rechecked according to LQAS, and if also workload is low, the samples will represent a large proportion of total smears performed.

## Slide 16: Sample Collection
Usually quarterly
May be more or less frequent
Division of annual sample by interval period
Ensure that total sample has been selected
Notes: Stress that sampling is divided over the year, usually per quarter. If sampling is less or more frequent, or visits were missed, this has to be made up for by collecting the required number to reach total annual samplesize, i.e. by selecting more slides during the next visit.
Specify on this slide the instruction concerning frequency and interval for your country.

## Slide 17: Key Messages
The purpose of rechecking is to screen for possible problems in AFB microscopy based on a sample of smears examined in routine work
Clear errors found may still be due to chance, but may also indicate problems; further investigations are needed only for those laboratories
The sample of routine slides should be as small as possible, representative and random
Rechecking requires a substantial investment of financial, material and human resources