## Slide 1: Module IDENTIFICATION AND MANAGEMENT OF DISCORDANT SLIDES

## Slide 2: Content Overview
Identification of discordants
Management of discordants
Validation of rechecking results
Identification and allocation of errors
Notes: Customisation of this presentation: it is better to replace the terms "first controller", "second controller", "coordinator" and "higher level" by the exact designations of these staff and level of the service.

## Slide 3: Classification of Discordants
Discordant slides are slides found positive (scanty, 1+, 2+ or 3+) by the microscopy centre and negative by the first controller or the reverse.
Quantification differences that need to be rechecked by a second controller are differences in positive grading of more than one step: scanty versus 2 + or 3+ and 1+ versus 3+.
Notes: Explain that this concerns discordants between the first controller and the laboratory that need to be counterchecked by a second controller. Stress that small differences of quantification of only one step in the scale are not considered discordant or error, and not sent for second control.

## Slide 4: Discordants Countercheck
Discordants between the first controller and the laboratories are counterchecked by the second controller
  to resolve discrepancies
  first controllers can make mistakes, so results need validation
  misconception that there should not be any errors; if no errors in large numbers rechecked, non-blinding or cheating may be suspected
  best at higher level to avoid bias
Notes: Stress that the second controller check is absolutely necessary to arrive at the most correct interpretation. Usually this requires that the second controller should be at a higher level than the first to avoid bias.

## Slide 5: Principle of Countercheck
Second controller knows both results, not which from the laboratory centre and which from first controller
Second controller uses both results as guidance
May require prolonged search to find or exclude AFB
Notes: Stress that the second controller does not need to be blinded as regard the two results. But (s)he should not know which results are from the laboratory and which from the first controller.

## Slide 6: Management of Discordants (1)
Rechecking coordinator
  Identifies discordants
  Lists discordant results of all microscopy centres under one first controller on discordants form
    Result 1 randomly for some entries of microscopy centre, others for results of first controller; reversing for result 2

## Slide 7: Management of Discordants (2)
Rechecking coordinator
  Requests discordant sides of all centres on discordant form from first controller packed in separate box
  Sends box to second controller
  No feedback yet to microscopy centres, unless no discordants identified
Notes: Stress that no feedback must be given to laboratories before the discordants have been examined by the second controller, since otherwise the errors cannot be defined or allocated to peripheral labs and first controller.

## Slide 8: Management of Discordants (3)
Second controller (1)
  Restains all ZN slides if restaining of all sample slides was not done at 1st control level
  Restains all auramine stained slides if fading was not protected since restaining
  Or restains all ZN and auramine stained slides restained at 1st control level if fading was not protected since restaining
Notes: Customisation: adapt to the restaining policy in your country.
Stress that restaining needs to be done now if it was not done earlier, for all discordants. But that it should be avoided as much as possible by proper keeping of the slides if it was done before first controls.

## Slide 9
Second controller (2)
  Examines the slides
    2 lengths for a difference negative versus clear positive (1+ to 3+)
    5 lengths for scanty versus negative
    for QE as required
      quantification of positive results, e.g. 98/200, 20/500
Management of Discordants (4)

## Slide 10
Second controller
  Notes quantified results on discordant form
  Adds qualitative remarks
Makes copy of form for file
Sends original form to rechecking coordinator
Management of Discordants (5)

## Slide 11
Rechecking coordinator
  Receives discordant form with both results from second controller
  Fills results on rechecking forms, one form for each of the laboratories
  Fills tables at the bottom of rechecking form with numbers of slides rechecked and errors identified, for laboratories centres and first controller
Management of Discordants (6)

## Slide 12: Validation of Results (1)
Validation essential before analysis and interpretation since controllers do not always perform well
Rechecking coordinator checks all results of a quarter:
    no discordants in many slides: blinded rechecking?
    more FN by 1st controller than the laboratories controlled: superficial examination?
    FP in many laboratories: quality of the second controller ?, restaining done ?
Notes: Stress the importance of validation. FNs for the 1st controller may be more than for all laboratories covered by that controller together. This may mean that the examination of the 1st controller has been too superficial. In this case FNs by the centres may have been missed by the 1st controller. Explain that under some conditions (rapid fading, staining problems) validation can only be done fairly if all smears were restained at 1st control level. Otherwise the first controller will have made false negative errors, because the AFB were not visible.

## Slide 13: Validation of Results (2)
Validation using 1-3+ FP smears
  Feedback from microscopists and visiting supervisors returning these slides to those who made the error
  May show positives missed by both controllers
    allows correction of results
    need to replace a second controller?
Notes: Stress that validation should also take into account the feedback from slides considered to be high FP mainly. The technicians or controllers who made the error will then sometimes show to the visiting supervisor that AFB are really there. Supervisors must report this to the coordinator, who will correct the results. If this happens regularly, the second controller is not sufficiently good and must be replaced.

## Slide 14: Classification and Definition of Errors
Classification and definition of errors found in cross-checking
Registered result
Final result
being controlled
negative
scanty
1+
2+
3+
negative
correct
LFN
HFN
HFN
HFN
scanty
LFP
correct
correct
QE
QE
1+
HFP
correct
correct
correct
QE
2+
HFP
QE
correct
correct
correct
3+
HFP
QE
QE
correct
correct
HFP:
high false positive, negative versus clearly positive result
HFN:
high false negative, positive versus totally negative result
LFP:
low false positive, negative versus scanty result
LFN:
low false negative, scanty versus totally negative result
QE:
quantification error, at least two steps difference in quantification
Notes: This table shows the definition of errors after counterchecking of discordants by the second controller and validation of the results. HFP and LFN are declared for a negative versus a high positive (1 to 3+) result; LFP and LFN are declared only for a negative versus a scanty result; QE concerns an error because of quantification at least 2 steps different in the scale. Give examples of those pointing them out in the table above.

## Slide 15: Analysis and Compilation of Errors
After rechecking of each series of slides
  Allows for early investigation and action if serious problems
  Provides opportunity to monitor whether centres with a serious problem improve during further checks
Only routine feedback if no or only few, minor errors are detected

## Slide 16: Key Messages
Discordant results between the first controller and the laboratory should be counterchecked by the second controller
The second controller will know the two results but must not know who those results belong to – to the laboratory or to the first controller
Validation of the rechecking results is needed to ensure the quality of the controls
Identification and allocation of errors should be done after rechecking of each series of slides