## Slide 1: Module REPORTING AND ANALYSIS OF AFB-SMEAR LABORATORIES PERFORMANCE, MANUAL SYSTEM

## Slide 2: Content Overview
Manual compilation, analysis and interpretation of rechecking results
Computer reporting, analysis and interpretation of rechecking results
Feedback, problem identification and solving

## Slide 3
MANUAL COMPILATION, ANALYSIS AND INTERPRETATION OF RECHECKING RESULTS

## Slide 4: Compilation, Reporting and Analysis
According to a manual system alone
Or together with a workbook
  Computerized
  National and (eventually) intermediate level
Compilation and analysis always quarterly and annually
Laboratory performance reports
  Independent of rechecking reports
  Essential when using the workbook

## Slide 5: Laboratory Performance Forms
Quarterly report: ”AFB laboratory performance and stock of consumables”
    Filled quarterly by each laboratory
    Send to higher level to compile area report
    Higher level compiles consolidated report
    Stock situation for estimation of essential supplies at intermediate level, NOT for calculation of supplies to be ordered from higher up
Quarterly / annual report “AFB laboratory performance”
    For intermediate level coordinator to report consolidated performance of labs to higher up
    Numbers of smears examined by type-diagnostic, follow-up- and result-pos., scanty, neg.
Notes: Customisation: change types and names of forms to be conform with your country's policy..
Stress that these laboratory performance reports are needed independent of rechecking reports. These provide essential information on workload and parameters related to the quality of work. Analysis of rechecking results, using the workbook, will only be possible with the data provided in the quarterly/annual report AFB laboratory performance.

## Slide 6: Quarterly Report AFB Lab. Performance and Stock of Consumables
Notes: Customisation: show this form only if in use. Replace this form by your country's adaptation.
Stress that the stock situation is meant to estimate the needs for essential supplies at the intermediary level, for automatic supply to the laboratories. The stock situation is not meant for reporting to higher up; the number of smears examined and the number of functional laboratories are used to calculate the supplies that need to be ordered from higher up.

## Slide 7: Quarterly Report AFB Laboratory Performance
Notes: Customisation: show this form only if in use. Replace this form by your country's adaptation.
Stress that this form is needed independent of rechecking results. It provides some essential information on workload and other parameters related to quality of the work in the laboratories of the network. However, for easy analysis, a computer spreadsheet is needed. Analysis of rechecking results using the computer workbook will not be possible without these data.

## Slide 8: Manual Rechecking Documents (1)
Form 1: Blinded Rechecking of Smear examinations for AFB
  Filled by supervisor taking the sample
  Registration of sampled slides for rechecking
  One form for each lab: one copy with results, one without results (for the 1st controller)
  Coordinator fills results on both copies after receiving 1st controller’s results
  Coordinator identifies discordant results
Notes: Customisation: specify the designation of supervisor collecting the samples, first controller and coordinator in your area. Add practical details as needed.

## Slide 9: Manual Rechecking Documents (2)
Form 2: List of Discordants
  Coordinator lists discordant slides on Form 2 with both results
    One or more labs under one controller on one form
    Column 1st and 2nd result switched for lab and 1st controller
  2nd controller receives form 2 with the discordant slides
  2nd controller enters results in “result” column and returns form 2 to coordinator
Notes: Customisation: specify the designation of first and second controller and coordinator in your area. Add practical details as needed.
Stress that it is very important to switch the result of the laboratory and that of 1st controller between the columns 1st result and 2nd result. Thus to use column 1st result for some results of the laboratory and for some results of the 1st controller.

## Slide 10: Manual Rechecking Documents (3)
  Coordinator adds 2nd controllers result to both copies of form 1
  Coordinator fills boxes on form 1, below slide list
  Coordinator completes form 1 by adding recommendations at bottom, depending on findings
  One copy for feedback to lab, one with coordinator for preparation of quarterly report (form 3)
Notes: Customisation: specify the designation of first and second controller and coordinator in your area. Add practical details as needed.
Stress that by filling the boxes below the slide listing, the totals on the right in the cross-tabulations must correspond to the counts for the different results as listed for the laboratory and 1st controller.

## Slide 11: Manual Rechecking Documents (4)
Form 3, Quarterly/Annual Report Form
  Compiles rechecking results for an area for all labs controlled
  Only summary counts, not individual slides
  Sent quarterly to higher level
  Can be omitted, if workbook is used and filled directly from form 1

## Slide 12: Blinded Rechecking Form 1
Notes: Customisation: replace this form by your country's adaptation.

## Slide 13: Discordants Form 2
Notes: Customisation: replace this form by your country's adaptation.

## Slide 14: Quarterly / Annual Rechecking Form 3
Notes: Customisation: replace this form by your country's adaptation.

## Slide 15: Analysis
Errors by type and centre for each series
Final analysis after full year sample
Interim analysis
  Feedback for continuous motivation
  Improve compliance, if applicable
  Further investigation if problems and remedial action
  Check on improvement of performance in following series
Notes: Stress that the LQAS criteria used to select the sample size should be applied for evaluation, but only after finishing the full sample of one year. Interim analysis should focus on clear problem labs, while assuring only motivating feedback to the others. Even so the difference in SPR between centres can cause bias with manual analysis of results from uniformly sized samples. This is corrected using a computer workbook for more refined analysis of the results.

## Slide 16: Error Frequencies
Not accurate per centre
Better for all centres of large area
By type; denominator all slides with +, -, or scanty result reported
  by laboratory
  by first controller
Notes: Explain that denominator for the first controller may be slightly different from that of the laboratory.

## Slide 17: Evaluation
No single agreement for all results
  Loss of valuable information
  Aim is not to score centres, but detection of specific problems
Notes: Do not combine false positive and false negative error rates (and maybe also the qualitative appreciations) into one single score. This may be quite misleading and in any case it hides important information necessary for the investigation and solving of problems.

## Slide 18: Validation
Comparison of sum of FN of all labs under a first controller with FN by controller
  Always
  Check on controller’s reliability
May be misleading
  In case positives were over sampled
  If restaining of discordants only
Notes: Explain that validation of controllers’ results is essential but can be misleading in the following settings:
when positives smears were added to the random samples, resulting in a higher SPR in the samples rechecked than in routine. In this case the controllers are at a disadvantage and must be allowed more FN
in settings where fading happens fast (climate, or poor staining), and only discordants were restained prior to second controls. The first controllers then have had no chance to detect some of the true positives that had faded again.
Mention that the computer analysis with the workbook will take into account differences in SPR from routine performance data.

## Slide 19: Interpretation
Annual report
  Number of errors by microscopy centre and first controller
  No HFP allowed; LFP ignored unless too frequent
  Not a single FN error allowed if d=0
  Interpretation and decision on corrective action on total numbers and type of errors
Calculation of error frequencies and performance indicators
  Not per centre, but for defined area
  At which level? Decision by NTP management
Notes: Explain that the interpretation according to criteria set in the LQAS system takes into account limitations of rechecking. Reproducibility is low for scanty results, and for this reason LFP are ignored if they occur at low frequency, similar to that seen in other centres and for the first controller. Moreover, finding of rare serious errors may not always indicate a true problem, so that the service has to set criteria to decide on the need for further investigation.

## Slide 20: Example of Annual Rechecking Report
Notes: This is an example of an annual report of microscopy centres under one first controller in an urban area. In the national TB control programme the acceptance number had been set at 0; 60 smears are randomly selected and rechecked per centre annually. Center D had 11 HFN and 2 LFN; centre G has 6 HFN and 1 LFN; both centers must be investigated urgently. Two centers have HFP: one centre (E) 1 HFP and one centre (F) 4 HFP. Centre E does not have LFP. Centre F has also 2 LFP. Only Centre F may have a serious problem in need of urgent investigation. All other centers except A have too many errors, although this seems less urgent.
Stress that serious problems observed in the quarterly reports should already be investigated at an early stage; one should not wait until the end of the year when the entire sample has been rechecked.

## Slide 21: Key Messages
Reporting and analysis of rechecking results can be done either manually or by means of the computerized tool (MS Excel based Workbook)
Properly filled in laboratory performance and rechecking reports (quarter / annual) provide a basis for the comprehensive analysis and evaluation of laboratory performance