## Slide 1: Module REPORTING AND ANALYSIS OF AFB-SMEAR LABORATORIES PERFORMANCE, COMPUTERISED SYSTEM

## Slide 2: Content Overview
Manual compilation, analysis and interpretation of rechecking results
Computer reporting, analysis and interpretation of rechecking results
Feedback, problem identification and solving

## Slide 3: COMPUTER REPORTING, ANALYSIS AND INTERPRETATION OF RECHECKING RESULTS

## Slide 4: Computer Compilation of Data
For use at national and (eventually) intermediate level
Automatic additions quarterly/annually
Automatic analysis of results by lab, by higher administrative level and by 1st controller if all data filled
Automatic correction for inaccuracies due to
  Uniform sample size
  Over-sampling of positives
  by converting FN rates to relative sensitivities
Notes: Customisation: specify at which level the data will be entered in a computer file, and how information will be transmitted to the higher level (manually filled reports, or already computerised). Define this clearly for each intermediate level.
Explain that the difference in SPR between centres can cause bias with manual analysis of results from uniformly sized samples. This is corrected using a computer workbook for more refined analysis of the results.

## Slide 5: Workbook Sheets
Menu
Set up
Q1 to Q4
Q1P to Q4P
YR EQA
YR P
YR CONTR
Analysis Labs
Summary Labs
District totals
Notes: Customisation: replace the term "District" in the last bullet by the true designation of the intermediate level for which totals will be analysed in your setting, if necessary.
The workbook sheets can be assessed through links in the opening Menu sheet. These sheets are labeled at the bottom.

## Slide 6: Menu
Notes: Customisation: replace the term "District" on line 2 of Tables by the true designation of the intermediate level for which totals will be analysed in your setting, if necessary. This has to be done in the workbook page itself, with copy / paste to here.
Explain that other sheets can be opened through links in Menu sheet

## Slide 7: Set Up
Notes: Customisation: replace the terms "Region" and "District" on top by the true designation of the intermediate levels for which totals will be analysed in your setting, if necessary. This has to be done in the workbook page itself, with copy / paste to here.
Explain that information filled in the set up sheet will automatically appear in the correct places throughout the workbook, wherein they cannot be changed or added. The list with arbitrary codes of the 1st controller should be replaced by real codes or names. These will then be available as a drop-down list in the appropriate place when filling the quarterly results of rechecking.

## Slide 8: Quarter 1 - Quarter 4
Notes: Explain that these sheets will be filled with quarterly results of rechecking. The names of the controlled labs and the district code will automatically appear from the set up sheet. Any additional name cannot be added here, but should be added in the set up sheet. Under evaluation of the microscopy labs” the numbers of smears rechecked (by result) and the number of errors must be filled. These should be copied from Form 3 or Form 1 of the manual system. The same is done for the first controller in the right side part. Only numbers should be entered in the boxes.

## Slide 9: Quarter 1P - Quarter 4P
Notes: Explain that these sheets will be filled from quarterly performance reports of the laboratories. Here the district codes and names of the labs are automatically shown. In the right side part the numbers of smears routinely examined in the labs, by result and by type, should be entered. Totals are not entered, these will be added up in the annual sheet.

## Slide 10: Year EQA
Notes: Explain that this sheet will show the totals of the quarterly rechecking data, in so far entered. Nothing in this sheet needs to be filled, it will automatically add up the quarters

## Slide 11: Year P
Notes: Explain that this sheet shows the totals and analysis of the routine laboratory performance data in so far data have been entered. The right part is an analysis of totals and prevalence of positive and scanty results, separately for diagnostic and follow-up smears. Nothing on this sheet needs to be entered.

## Slide 12: Year Contr.
Notes: Explain that this sheet shows the totals of the quarterly rechecking data, in so far entered. Each controller is shown individually. The “percent true positive detected” and “percent true positives/all positives” analyses their performance in rechecking. Nothing in this sheet needs to be filled. Newly entered data will be calculated only after reopening the workbook.

## Slide 13: Analysis Labs
Notes: Explain that this sheet shows analysis of routine AFB microscopy, as well as the findings from rechecking by laboratory for all quarters together. The column “smears examined during the year” shows total smears and percent positive and scanty, without distinction between diagnostic and follow-up smears. The next column shows the totals of smears rechecked, by results. The right column shows selected results of rechecking: number of HFP, HFN and LFN, and their analysis: “detection proportional to controllers” and “percent true positives/all positives”. In the top right corner appears an average estimate of controllers performance: ”percentage true positive/scanty overall detected by the controllers”. The analysis columns have been given color coded to automatically highlight unsatisfactory performance. The colors can be changed, via the Format menu, as also the set level of (un)satisfactory performance.

## Slide 14: Summary Labs
Notes: Explain that this sheet automatically recapitulates a summary of performance and quality of all laboratories, in so far they were included in the performance and rechecking reports. This includes classification of laboratories based on quality of positive (“true positive”) and negative (“detection”) results. This report may particularly be useful for (quarterly)/annual reports.

## Slide 15: District Totals
Notes: Explain that this sheet shows totals for the administrative subunits when these were specified. It adds up automatically during the year and is automatically refreshed when the workbook is reopened.
In a larger version of the workbook this sheet is called “Admin_Div_III_Totals” and there are two more of these sehhet to prepare the summaries by higher administrative division,”Admin_Div_II_Totals” and Admin_Div_I_Totals”. This large workbook can be used to compile a national report, filling it directly manually, or by copying and pasting from several smaller workbooks filled at intermediate level.

## Slide 16: Analysis
The analysis includes
  Total workload
  Prevalence of positives among diagnostic and follow-up smears
  Total prevalence of positive and scanty positive smears
The analysis takes into account
  Differences in prevalence of positives between labs
  Differences in prevalence of positives between samples presented to 1st controller and the routine slides

## Slide 17: Interpretation (1)
Conversion of error rates to performance indicators
  Check on performance of controllers: percentage true positives detected by controllers or relative sensitivity of first controllers
  Quality of work of each lab compared to controller: detection by labs proportional to the controllers or ratio of relative sensitivity of the labs versus controllers
  Accuracy of a positive result: percentage of true positives out of all positive results or positive predictive value of the labs

## Slide 18: Iinterpretation (2)
Percent true positives detected by first controllers:
  Controllers’ true positive / (True positive + False negative) x 100%
  Should be around 95%
Notes: This indicator is a check on the performance of the controllers.

## Slide 19: Iinterpretation (3)
Detection by centres proportional to the controllers
  same percent detection calculation per lab, then divided by average first controllers (ratio)
  1.00= equal good work by centre and controller
  >1.00= better work by centre than controller
  The lower the worse the performance of the centre
  If e.g 0.65= centre detects 65% of + slides compared to controller
Notes: This indicator compares the quality of work of each lab. to that of the controller.

## Slide 20: Interpretation (4)
Percent true positives out of all positives
  ((True positive / (True positive + False positive)), x 100%
  100% = a positive result is fully reliable
  The lower, the worse the performance of the lab, but with few positives rechecked this indicator may be misleading
Notes: This indicator is a check on the accuracy of a positive result. Scanty results are not included, as these cannot always be confirmed by rechecking. The indicator will be too imprecise and will thus not be shown if less than 5 positives were rechecked.

## Slide 21: Unsatisfactory Performance Criteria
To be defined by NTP management
Recommended
  Annual analysis
    < 0.75 detection proportional to controller
    < 95% true positives
  Quarterly analysis
    Centres with (almost) all 1+ to 3+ FP
    < 0.60 detection proportional to controller
Notes: Customisation: eventually change the minimum criteria to the standards set by your programme. However, explain that these are also meant as triggers for action. Labs remaining below the minimum will need an (urgent) problem solving visit.
With few positives rechecked, the absolute number of HFP should be taken into consideration, as there will be no percentage on accuracy of positives.

## Slide 22: Example of a Workbook (1)
Notes: This is the set up sheet of the workbook. The seven laboratories in the urban/rural Dhaka division are the same as presented in the manual reporting and analysis of rechecking results (form3).

## Slide 23: Example of a Workbook (2)
Division
Second controller
Year
EQA coordinator
Name of the
Controller
District
controlled labs
Pos.
Scanty
Neg.
HFP
LFP
HFN
LFN
QE
ID
Pos.
Scanty
Neg.
HFP
LFP
HFN
LFN
QE
Urban
AB
4
56
Ahmed
4
1
55
1
Urban
BC
3
57
2
1
Ahmed
5
55
Urban
CD
5
1
54
1
3
1
Ahmed
8
2
50
Rural
DE
3
1
56
11
2
3
Mourad
14
2
44
1
Rural
EF
8
2
50
1
1
2
Mourad
9
3
48
1
Rural
FG
15
2
43
4
2
2
Mourad
11
4
45
Rural
GH
4
56
6
1
4
Mourad
10
1
48
2
Division
42
6
372
5
3
23
6
10
61
13
345
3
2
RE-CHECKING OF SPUTUM SMEARS FOR AFB
QUARTERLY COMPILATION SHEET
EVALUATION OF THE MICROSCOPY LABS
Dhaka
2006
Results reported for
rechecked smears (#)
Errors detected in EQA (#)
EVALUATION OF THE FIRST CONTROLLERS
Results reported for
rechecked smears (#)
Errors detected in EQA (#)
Notes: These are the rechecking results for the 7 laboratories for the year, peripheral labs as well as first controllers.

## Slide 24: Example of a Workbook (3)
Division
Year
Name of the
District
controlled labs
Pos.
Scanty
Neg.
Pos.
Scanty
Neg.
Urban
AB
196
37
1498
2
2
170
Urban
BC
50
318
1
37
Urban
CD
323
26
2478
1
3
306
Rural
DE
104
17
1271
1
4
135
Rural
EF
204
12
2426
2
6
272
Rural
FG
304
3273
2
7
373
Rural
GH
293
15
2653
2
306
Division
1474
107
13917
10
23
1599
Diagnosis
Follow-up
2006
PERFORMANCE OF SPUTUM SMEAR LABORATORIES
QUARTERLY COMPILATION SHEET
Dhaka
NUMBERS OF SMEARS DONE BY THE LAB
Notes: These are the performance reports for the 7 laboratories for the year.

## Slide 25: Example of a Workbook (4)
Notes: This shows how the workbook has analysed the annual totals for the labs, indicating excessive numbers of errors according to pre-set colour codes. The colours can be defined as perferred by criteria as preferred. This analysis will always appear and can be used also to identify possible problem labs if the individual performance data are not available, but the analysis is less objective since it doesn't take into account the differences in positivity rates.
Rates for the totals of all labs together are calculated at the bottom. It makes no sense to try the same per lab, samples are too small and rates very imprecise.

## Slide 26
Example of a Workbook (5)
Notes: This shows how the workbook has analysed the performance reports of the the labs, with anual totals and calculation of proportions. The rates of positives and / or scanty in diagnostic versus follow-up smears, besides the total smears done (so workload) are important indicators. Also here colour codes have been defined to show aberrant values more clearly.

## Slide 27
Example of a Workbook (6)
Notes: This shows how the workbook has analysed the performance reports of the first controllers, separately and together. This allows the identification of poor controllers. Rates are calculated for the controller totals only.

## Slide 28
Example of a Workbook (7)
Notes: The annual analysis of the 7 laboratories of the urban/rural area shows in the first three colums next to the names also an analysis of the routine performance for the same centres. The following three columns show totals of slides rechecked by result. On the right hand side are columns showing the most important errors detected as absolute numbers, and also with their conversion to detection proportional to the controllers, and the percent true positives. The box on top right shows the average detection by the first controllers, used to calculate the proportional detection by the centres. The sheet automatically puts colour codes to highlight inadequate performance, which can be adapted to the needs of the country. In this example the criteria for unsatisfactory performance in the annual analysis were defined as < 0.75 detection proportional to the controler and < 95% true positives.
If only very few positives were rechecked, the values of true positives detected (right hand column) may be misleading, and more attention should be paid to the absolute number of HFP.

## Slide 29
Example of a Workbook (8)
Notes: This is a summary report for the whole administrative area covered by the workbook and the full year (as far as entered in the workbook). Only the main information is given, without showing names, numbers or rates for individual labs, controllers or subdivisions. This is meant for the global NTP report, to show what was done for EQA, and how the labs perform overall (i.e. number and porportion remaining below a set minimum performance level), which can then be compared with earlier years.

## Slide 30: Key Messages
Reporting and analysis of rechecking results can be done either manually or by means of the computerized tool (MS Excel based Workbook)
The Workbook is intended for use at the national and, eventually, also at the intermediate level
Properly filled in laboratory performance and rechecking reports (quarter / annual) provide a basis for the comprehensive analysis and evaluation of laboratory performance