## Slide 1: Module ANALYSIS OF AFB-SMEAR LABORATORIES PERFORMANCE, INTERPRETATION OF RESULTS AND FEEDBACK

## Slide 2: Content Overview
Manual compilation, analysis and interpretation of rechecking results
Computer reporting, analysis and interpretation of rechecking results
Feedback, problem identification and solving

## Slide 3: FEEDBACK, PROBLEM IDENTIFICATION AND SOLVING

## Slide 4: Feedback (1)
Regular feedback
  Indispensable
  Encouragement and motivation
  Improving performance, if applicable
  No criticism unless serious negligence/bad will
Visit by TB supervisor
  Feedback; return of slides with serious errors
  May identify possible causes of errors with checklist
  May propose remedy, such as replacement of microscope
Notes: Customisation: specify the exact designation and tasks of the general (non-lab specialist) TB supervisor in your programme

## Slide 5: Feedback (2)
Identify priority centres for problem solving
  Several HFP and/or HFN
  HFN and many LFN, or just many LFN
  Many LFP
On-site visit by an expert for identification of causes and problem solving
Notes: Customisation: specify the exact designation lab expert in your programme

## Slide 6: Problem Identification and Solving (1)
In case of unsatisfactory performance of microscopy centres
  Identify possible causes
  Investigate
  Take appropriate action
Consider overall pattern of errors: (many) HFP, HFN, QE, combination of errors

## Slide 7: Problem Identification and Solving (2)
Many (or almost all) HFP and HFN
Possible causes
  Lack of training
  Unusable microscope
  Smears not examined
Investigations
  Examine 3+ with that microscope
  Request staff to examine 2+, or 3+ and negative smear with good microscope

## Slide 8: Problem Identification and Solving (3)
Occasional HFP
Possible causes
  Administrative error
  Failure of controllers
Investigation
  Compare lab. register with rechecking list for correct number and result

## Slide 9: Problem Identification and Solving (4)
Few HFP, with/without LFP
Possible causes
  Administrative error
  Recognition of AFB?
  No systematic restaining
  Copying positive result 1st smear to 2nd and/or 3rd smear (workload?)
Investigations
  Check admin. procedures: use of lab register, sputum request form, labeling sputum container
  Inconsistent smear results: regular isolated + or scanty?
  Restain and re-examine HFP to exclude that fading caused confusion and that it is not true FP

## Slide 10: Problem Identification and Solving (5)
Rare LFP
  Ignore if at frequency comparable to other centres and controller

## Slide 11: Problem Identification and Solving (6)
Several LFP, with/without low grade HFP
Possible causes
  Bad microscope, artifacts taken as AFB?
  Lack of experience
  Contaminated carbol fuchsin stain
  Poor counterchecks - FN by both controllers
Investigations
  Return FP to microscopy centre for showing AFB
  Test carbol fuchsin on known negative smear

## Slide 12: Problem Identification and Solving (7)
Single HFN
Possible causes
  Administrative error
  Smear not examined, 2nd and 3rd smear copied (workload?)
Investigations
  Check administrative procedures
  Check workload
  Smear not examined: difficult to prove

## Slide 13: Problem Identification and Solving (8)
Several HFN and/or LFN and/or low quantification
Possible causes
  Very thick smear
  Poor light in microscope
  Bad stain or poor staining (if smears were all restained)
  Contaminated methylene blue or rinsing water (after restaining)
  Superficial / no examination

## Slide 14: Problem Identification and Solving (9)
Several HFN and/or LFN and/or low quantification
Investigations
  Check thickness of smears
  Check microscope: position condenser and diaphragm and remove filters
  Check carbolfuchsin stain: dark, red, shiny when poured on slide
  Check if AFB are well stained in fresh not restained pos. smear
  Check staining procedure: sufficient time, heating
  Use methylene blue on known neg-atypical AFB?
  Check workload (overload)
  If all above fail to show cause; superficial reading may be the cause

## Slide 15: Problem Identification and Solving (10)
Serious QE
Possible causes
  Poor stain/staining
  Problems with microscope, only few AFB in high positive smears
  Lack of quantification skills
Investigations
  Check if AFB are well stained with carbol fuchsin
  Observe staining procedure: sufficient time, heating
  Ask staff to quantify a few positives

## Slide 16: Key Messages
Reporting and analysis of rechecking results can be done either manually or by means of the computerized tool (MS Excel based Workbook)
The Workbook is intended for use at the national and, eventually, also at the intermediate level
Properly filled in laboratory performance and rechecking reports (quarter / annual) provide a basis for the comprehensive analysis and evaluation of laboratory performance
Regular feedback to laboratories is very important for improving or maintaining motivation and performance
A finding of poor performance has to be completed by a problem identification and solving visit. The problem and its cause(s) are rarely clear from rechecking as such.