## Slide 1: Module ON-SITE SUPERVISION OVERVIEW

## Slide 2: Content Overview
What is on-site supervision?
Advantages and disadvantages of on-site supervision
Organization of supervision
  Who should supervise microscopy laboratories?
  When to supervise?
  What to supervise: laboratory operational elements to be checked
Feedback

## Slide 3: On-Site Supervision
An essential component of an EQA program since it is the best method to obtain a realistic picture of the conditions and practices in the laboratory
Aimed at problem solving
Provides continuing education
Motivates staff to improve performance
Notes: STATE that the main purpose of on-site supervision is to make a direct assessment of a peripheral microscopy laboratory under normal working conditions in order to check that it is operating in accordance with standards set down by NTP/ NRL.
STRESS that supervision must be supportive, checking for and helping to solve problems. It is also a means of continuing education since during training some details may not have been well understood and supervision can help filling up the gaps. Supervision needs a positive attitude and good understanding of the subject.

## Slide 4: Advantages / Disadvantages
ADVANTAGES:
  Ability to identify source of errors detected by rechecking and/or panel testing
  Ability to initiate prompt corrective actions to resolve problems
  Motivation of staff
  Educational aspect
DISADVANTAGES:
  Expensive and labor intensive
  Is impracticable if assigned only to NRL
Notes: STRESS that it is difficult to find good supervisors. Good supervision is not that easy to properly implement. NRL cannot do it on its own, therefore the intermediate level should also be involved.

## Slide 5: General Organization
Who??
  professional laboratory specialist from a higher level laboratory
  TB supervisors
When??
  frequency can be limited by resources
  by laboratory specialist
    annual routine visit is sufficient
  by TB supervisor:
    quarterly
  most sufficient: frequent or urgent visits to laboratories suspected of having serious problems
Notes: STATE that TB supervisors must also visit labs even just briefly, to enquire about problems. If properly trained they can confidently conduct on-site supervision - take rechecking samples, distribute panels, give routine rechecking feedback, etc. With some exercise, they could even check the quality of smears and staining.

## Slide 6: Different Types of Supervisory Visits: Summary
Who can conduct? | Frequency | Purpose/ main activities
TB supervisor | quarterly | General lab check Supplies inventory / microscopes check Collection of slides for blinded rechecking Distribution of panels
Professional laboratory specialist from a higher level laboratory | preferably annually | Comprehensive assessment Implementation of corrective actions Training
 | upon identification of very poor performance based on results of panel testing or blinded rechecking | 
 | in the context of surveys | 

## Slide 7: Laboratory Elements to Be Evaluated by TB Supervisors
Availability of SOP
Supply of reagents
Supply of consumables
Equipment
Safety practices
QC practices
Notes: STATE that supervisors should make sure that written standard operating procedures are available, supply of consumables and reagents is adequate, reagents are within the expiration date. Supervisors should also make sure that the microscope is functioning. TB supervisors must be familiar with simple microscope function, and be able to visualize a clear image through the microscope lens. Supervisors should make sure that laboratory safety practices are observed. Supervisors should also check internal quality control procedures and assure that positive and negative control slides are used with all newly made batches of stains as well as with each daily batch of smears.
NOTE that each country should be decide on the scope of work for TB supervisor when he/she visits laboratories to evaluate laboratory performance.

## Slide 8: Laboratory Elements to Be Evaluated by TB Supervisors (cont.)
Record keeping
Evaluation of workload and proportion of positive smears
Storage of slides for blinded rechecking
Training of laboratory staff
  adequate training, refresher courses?
Corrective actions:
  are they recommended when appropriate?
Notes: EXPLAIN that supervisors should pay attention to registers and recording forms and check if record keeping is accurate and consistent with NTP requirements, if patients results are promptly reported to clinicians, if suspects recorded in the laboratory register as smear positive are recorded in the TB district register. Supervisors should evaluate workload and calculate proportion of positive smears, make sure that staff has received adequate training and corrective actions are recommended when appropriate
NOTE that supervisors should also check whether smears are properly stored for blinded rechecking. Supervisors should also be able to collect an appropriate sample of slides to be forwarded to NRL.

## Slide 9: Laboratory Elements to Be Evaluated by Laboratory Supervisors
In addition to all operational elements listed above for TB supervisors, laboratory supervisors should:
Evaluate
  sputum collection procedures
  smear preparation, staining, and reading
Recheck several positive and negative smears to evaluate:
  quality of staining, smear thickness, smear size and results
Review results of panel testing and/or rechecking.
Provide suggestions / implement corrective actions
Notes: ADVISE that it is better to observe smearing, staining and microscopy procedures without asking questions – to check whether technicians follow NTP guidelines or not. Then ask questions to differentiate lack of knowledge (needs training) from non-observance of guidelines (no need of training).

## Slide 10: On-Site Supervision: Important Issues (I)
Understanding of the rationale for each item to be checked
  Why this or that procedure is evaluated?
  How the findings can be interpreted?
  What are the consequences?
  What are the possible further checks and actions?
Use of checklists
  training of supervisors on how to use checklists
Capability and capacity to implement necessary corrective actions
Notes: STATE that checklists are the instrument that helps improve efficiency of on-site supervision and provide the means for reporting back to both laboratory staff and NTP. Checklists will help supervisors not to forget what laboratory procedures / areas they should look at during the visit but at the same time checklists will help avoid a subjective opinion of a supervisor. NTP should ensure sufficient training for using standard checklists

## Slide 11: On-Site Supervision: Important Issues (II)
Required:
  experienced supervisors for trouble-shooting and critical areas 
  training of TB supervisors and laboratory supervisors and evaluation of their work
Recommended:
  problem-oriented approach:
    checking specific areas known or suspected (from rechecking and / or panel testing results) to have problems

## Slide 12: Feedback
Provide verbal feedback to staff
Inform about negative as well as positive observations
Offer suggestions to problem solving
Document major recommendations
Plan a follow-up visit
Notes: EXPLAIN that the concise short report summarizing the main findings and providing recommendations should be prepared. The report could be a part of a checklist. The original report should be forwarded to the district NTP coordinator. The regional laboratory (and NRL) must also be aware of all significant findings. A copy of the checklist / report should be kept in the peripheral laboratory for reference.

## Slide 13: Key Messages
On-site supervision is an essential component of AFB smear microscopy EQA
There are two categories of a supervisory visit – by a laboratory professional and by a TB supervisor
Implementing on-site supervision will require training of supervisors and evaluation of their work
Standard checklists help ensure that assessments are carried out in a consistent and structured format, provided that supervisors are properly trained